Procedure to configure GSM FWP for Internet.

Step -1.

Connect GSM FWP to PC by means of USB cord.

Switch on the instrument if off.

Run  set up.exe file from CD provided with GSM FWP

On successful run of set up PC should restart.

Step -2

Go to control Panel- Phones and modems-Add modem

Tick don’t detect my modem.

Choose Standards Modem 33600 from available list.

Select com port [5, 6,…] which is newly added on setup.exe run.

Go to tab Advanced

Under extra initialization setting write –

AT+CGDCONT=1,”IP”,”bsnlnet”

Step-3

Create dial up connection.

Input dialing number *99***1#

Step-4

Right click dial up connection

Go to properties

Configure modem

Remove all checks[ticks] in boxes if available.

Now you can access internet using this dial up connection.